## Slide 1: LED flashing without delay() function

## Slide 2: Hardvare
Only LED on pin 13 is used, other hardvare is not needed.
digitalWrite(13, HIGH);
delay (2000); // wait 2s from now
digitalWrite(13, LOW);
delay (5000); // wait 5s from now
// no common referent time!!!

## Slide 3: millis()
One of the most powerful Arduino functions.
This function contains the number of elapsed milliseconds since power was applied, or since the last reset.
The idea behind millis() is similar to measuring current time: the time tells us how much time elapsed since midnight.

## Slide 4: delay() vs. millis()
delay(): the system waits for certain amount of time.
millis(): we ask how much time elapsed?

## Slide 5: Example 1
void setup() {
pinMode(13, OUTPUT);
}
void loop() {
digitalWrite(13, HIGH); // turn the LED on
delay(1000); // wait for a second
digitalWrite(13, LOW); // turn the LED off
delay(1000); // wait for a second
}
// The code is each time blocked for 1000ms.

## Slide 6: Example 2
We use the delay() function, but only for 1ms inside the loop.
void setup() {
pinMode(13, OUTPUT);
}
void loop() {
digitalWrite(13, HIGH); // turn the LED on
for (int x=0; x < 1000; x++) { // Wait for 1 second
delay(1);
}
digitalWrite(13, LOW); // turn the LED off
for (int x=0; x < 1000; x++) { // Wait for 1 second
delay(1);
}
}
It is possible to
call other
functions inside
the for loop,
but it will affect
the delay.

## Slide 7: Example 3: LED flash using millis() function
unsigned long interval=1000; // the time we need to wait
unsigned long previousMillis=0; // millis() returns an unsigned long.
bool ledState = false; // state variable for the LED
void setup() {
pinMode(13, OUTPUT);
digitalWrite(13, ledState);
}
void loop() {
unsigned long currentMillis = millis(); // grab current time
// check if "interval" time has passed (1000 milliseconds)
if ((unsigned long)(currentMillis - previousMillis) >= interval) {
ledState = !ledState; // "toggles" the state
digitalWrite(13, ledState); // sets the LED based on ledState
// save the "current" time
previousMillis = millis();
}
}

## Slide 8: Example 4: flashing two LEDS using millis() function
// each "event" (LED) gets their own tracking
// variable
unsigned long previousMillisLED12=0;
unsigned long previousMillisLED13=0;
// different intervals for each LED
int intervalLED12 = 500;
int intervalLED13 = 1000;
// each LED gets a state varaible
boolean LED13state = false;
// the LED will turn ON inthe first iteration of loop()
boolean LED12state = false;
// need to seed the light to be OFF
void setup() {
pinMode(13, OUTPUT);
pinMode(12, OUTPUT);
}
void loop() {
// get current time stamp
// only need one for both if-statements
unsigned long currentMillis = millis();
// time to toggle LED on Pin 12?
if ((unsigned long)(currentMillis - previousMillisLED12) >= intervalLED12) {
LED12state = !LED12state;
digitalWrite(12, LED12state);
// save current time to pin 12's previousMillis
previousMillisLED12 = currentMillis;
}
// time to toggle LED on Pin 13?
if ((unsigned long)(currentMillis - previousMillisLED13) >= intervalLED13) {
LED13state = !LED13state;
digitalWrite(13, LED13state);
// save current time to pin 12's previousMillis
previousMillisLED13 = currentMillis;
}
}
LEDs are connected to pins 12 and 13. Flashing intervals are different.

## Slide 9: Button press
LED on pin 13, resistor 220Ω.
2-ground: 10kΩ, 2-VCC pushbutton
const int buttonPin = 2;
const int ledPin = 13;
int buttonState = 0;
void setup() {
pinMode (ledPin, OUTPUT);
pinMode (buttonPin, INPUT);
}
void loop() {
buttonState = digitalRead(buttonPin);
if (buttonState == HIGH) {
digitalWrite(ledPin, HIGH);
}
else {
digitalWrite(ledPin, LOW);
}
}
Change the program so the number of presses is written on the Serial monitor.