## Slide 1: Variables

## Slide 2: Variable
The variable is a location in memory with a given symbolic name. This location can be filled, or left empty. It is used to store values of different type.
Variable are important because we can change (vary) their content during the execution of the program. Constant values can not be changed.

## Slide 3: Variable type
The type of the variable defines the nature of the data stored. Based on the type, the amount of memory space is determined for the variable.
The C programming language has around 10 different data types.

## Slide 4: Type of variable
boolean (false or true) – 1 byte
char (stores ‘a’ as number – ASCII) – 1 byte
byte (8-bit unsigned data, 0-255)
int (2-bytes, signed -32768 - +32767
unsigned 0-65535)
word same as unsigned int

## Slide 5: Type of variable
long (4 bytes signed -2147483648-2147483647 unsigned 0-4294967295)
float (4-bytes signed -3.4028235 E+38-3.4028246E+38)
double (same as float with double precision)
array – set of same type elements, access through index,
Size: (number of elements) x (type size)

## Slide 6: Roll-over
If we increase the value of the variable over the maximum value for that type, it will start from the beginning of the interval.
int myInt = 32767; // maximum
// value for int
myInt = myInt + 1; // myInt now has
// value -32768
The same happens when subtracting.

## Slide 7: Declaration and definition
Declaration and definition is NOT SAME!!!
Declaration of the variable is when we tell the type and (sometimes) the dimension of the variable.

## Slide 8: Declaration and definition
In C programming language the variable must be declared before use.
If we forget, the compiler will return an error.

## Slide 9: Declaration and definition - examples
bool myVariable; // declaration
myVariable = true; // definition by
// assigning value
char myChar = ’U’ // declaration and
// definition // (ASCII value of
// ‘U’=85)
int ledPin = 8;
byte myByte = B10111; // 23 in binary
// notation

## Slide 10: Definicija i deklaracija
long myLong = -123;
float myFloat = -123456.1;
Definition is value assignment to previously reserved memory location for that variable.

## Slide 11: S.O.S. project
Hardvare: LED connected to pin 12 and resistor 220Ω.
Softvare: program that flashes the LED according to Morse S.O.S. symbols
S: “. . .”, O: “- - -”, S: “. . .”

## Slide 12: S.O.S. project
int ledPin = 12;
void setup () {
pinMode(ledPin, OUTPUT);
}
void loop () {
digitalWrite (ledPin, HIGH);
delay(200); // dot
digitalWrite (ledPin, LOW);
delay(200);
digitalWrite (ledPin, HIGH);
delay(200);
digitalWrite (ledPin, LOW);
delay(200);
digitalWrite (ledPin, HIGH);
delay(200);
digitalWrite (ledPin, LOW);
delay(500);
digitalWrite (ledPin, HIGH);
delay(500); // dash
digitalWrite (ledPin, LOW);
delay(500);
.
.
.
}

## Slide 13: S. O. S. project
4 lines are constantly repeating:
HIGH, delay, LOW, delay, …
delay is either 200ms (dot), or 500ms (dash)
The code will be shorter and more efficient if we write a function for repeating operations.
We will name the function flash, and call it with duration which is either 200 or 500 (milliseconds).

## Slide 14: Function flash
void flash (int duration)
{
digitalWrite (ledPin, HIGH);
delay (duration);
digitalWrite (ledPin, LOW);
delay (duration);
}

## Slide 15: New loop function
void loop ()
{
flash (200); flash (200); flash (200); // S
delay (300);
flash (500); flash (500); flash (500); // O
flash (200); flash (200); flash (200); // S
delay (1000);
}

## Slide 16: New program using flash function
int ledPin = 12;
void setup () {
pinMode (ledPin, OUTPUT);
}
void loop ()
{
// S
flash (200); flash (200); flash (200);
delay (300);
// O
flash (500); flash (500); flash (500);
// S
flash (200); flash (200); flash (200);
delay (1000);
}
void flash (int duration)
{
digitalWrite (ledPin, HIGH);
delay (duration);
digitalWrite (ledPin, LOW);
delay (duration);
}

## Slide 17: Loops
Repeat group of instructions until a condition is met.
For letter “S”, the S. O. S. project turned the LED on and off only 3 times. What if hundreds of flashes should heve done?
We use for loops.

## Slide 18: “for” loop
We use it when in advance we know how many repetitions there will be.
Syntax:
for (int i = 0; i < 100; i ++)
{
flash(200);
}
Variable
(declaration of the counting variable and definition of the initial value – 0)
The condition to be
met to stay in the loop.
In this case until “i”
is smaller than100.
What to do after each
Passing through the loop.
In this case increase
“i” by 1.

## Slide 19: “while” loop
The previous task could be done using while loop.
To stay in the loop the expression in the bracket must be true, otherwise the program continues after the bracket.
int i = 0;
while (i < 100)
{
flash(200);
i ++;
}
Instructions between brackets are called “block”.

## Slide 20: Arrays
Arrays are suitable for storing multiple values. So far variables contained only one value (usually int).
The array is a variable with multiple values, and can be accessed through position inside the array.
The indexing of arrays start with 0.

## Slide 21: Arrays
We’ll make a list of durations of Morse symbols (200ms i 500ms).
int durations [] = {200, 200, 200, 500, 500, 500, 200, 200, 200};
If we define the content immediately, it is not necessary to define the length of the array.
If we do not define, then
int durations [10];

## Slide 22: New loop()
void loop ()
{
for (int i = 0; i < 9; i ++)
{
flash (durations [i]);
}
delay(1000);
}